SPECIFICATION

Section 07900/079500

Previous 05800

Wabo® FastWall

Model “EWH” Wall and Ceiling

Expansion Control Systems

PART 1 - GENERAL

1.01	Work Included

A.	The work shall consist of furnishing and installing expansion joints in accordance with the details shown on the plans and the requirements of the specifications.  The joints are proprietary designs utilizing preformed metal components, gaskets and fastening strips.

B.	Related Work

- Drywall

- Miscellaneous and ornamental metals

- Flashing and sheet metal

- Interior Finishes

1.02	Submittals

A.	Template Drawings - Submit typical expansion joint cross-section(s) indicating pertinent dimensioning, general construction, component connections, and anchorage methods.

1.03	Product Delivery, Storage and Handling

A.	Deliver products in each manufacturer's original, intact, labeled containers and store under cover in a dry location until installed. Store off the ground, protect from weather and construction activities.

1.04	Acceptable Manufacturer

- All joints shall be as designed and manufactured by Watson Bowman Acme, 95 Pineview Drive, Amherst, New York 14228.

B.	Alternate manufacturers and their products will be considered, provided they meet the design concept and are produced of materials that are equal to or superior to those called for in the base product specification.

C.	Any proposed alternate systems must be submitted and receive approval 21 days prior to the bid.  All post bid submittals will not be considered.  This submission shall be in accordance with MATERIALS AND SUBSTITUTIONS.

- Any manufacturer wishing to submit for prior approval must provide the following:

1.	A working 6” sample of the proposed system with a letter describing how system is considered superior to the specified system.

2.	A project proposal drawing that illustrates the recommended alternate system installed in the wall or ceiling construction that is specific to the project. Typical catalog cut sections will not be considered.

3.	Verifiable list of prior installations showing prior and successful experience with the proposed systems.

4.	Any substitution products not adhering to all specification requirements within, will not be considered.

  - Quality Assurance

A.	Manufacturer: Shall be ISO-9001:2015 certified and shall provide written confirmation that a formal Quality Management System and Quality Processes have been adopted in the areas of, (but not limited to) engineering, manufacturing, quality control and customer service for all processes, products, and their components. Alternate manufacturers will be considered provided they submit written proof that they are ISO 9001:2015 certified prior to project bid date. Manufacturers in the process of obtaining certification will not be considered.

B.    Manufacturer: Shall have a minimum ten (10) years experience specializing in the design and manufacture of Architectural Expansion Control Systems.

C.    Application: The specified expansion control systems shall be installed by a          factory trained installer certified in the proper installation of the expansion control and fire barrier systems.

PART 2 - PRODUCT

2.01	General

A.	Provide wall and ceiling expansion control system that accommodates two directional thermal movement with a variety of color finishes available to compliment adjacent finish surface treatments. Provide manufacturer’s system where hardware is hidden from view. The system shall be capable of following changes in direction to achieve a “corridor wrap” concept in high visible areas.

For walls and ceilings furnish Wabo® FastWall Expansion Control System, Model “EWH” as manufactured by Watson Bowman Acme and as indicated on drawings.

2.02	Components and Materials

A.	Exposed Cover - Materials shall be aluminum conforming to properties of ASTM B221 6063-T5.

B.	Slide Gasket - Material shall be a polyvinyl chloride (PVC) extruded profile. Design gasket to mechanically lock into continuous channel of aluminum cover.

C.    Base Extrusion – Material shall be a rigid polyvinyl chloride extruded profile.

D.	Anchors - Supplied by others. Contractor shall install appropriate anchor to accommodate wall and/or ceiling construction. For gypsum wallboard construction, manufacturer recommends standard drywall screws of sufficient length. Maximum spacing shall be 18” o.c.

- For masonry block or concrete construction utilize No. 12 diameter x 1 ¾” lg. (min.) flat head threaded concrete anchor. Anchor spacing at 18” o.c. maximum.

E.	Accessories - Provide necessary and related parts required for complete installation.

F	Fire Barrier Assembly - Designed for indicated or required dynamic structural movement without material degradation or fatigue. Tested in maximum joint width conditions with a field splice as a component of expansion joint cover in accordance with ASTM E-119 at a full rated period by a nationally recognized testing and inspecting organization. Supply ThermoShield Fire Barrier as governed by joint opening and fire rating.

2.03		Fabrication

A.	Extrusions to be shipped in standard 10 ft. lengths and shall be cut to length on jobsite where required.  Profiles shall be miter cut in the field to conform to directional changes unless otherwise contracted with expansion joint manufacturer.

B.	Slide Gasket shall be shipped in the longest practical continuous length in manufacturer’s standard shipping carton.

C.	Fire Barriers - Ship manufacturer’s standard assembly for the required hourly rating.  Fire barrier shall be miter cut in the field to accommodate changes in direction.

2.04	Finishes

A.	Exposed Cover

- Aluminum

Standard - Clear anodized finish in accordance with AA-M10 C22 A31 Class II (0.4 - 0.7 thick anodic coating).

Optional:

Aluminum - Color anodize.

ColorChoice with matte or bright finish. Select from     manufacturers standard color selection chart.

PART 3 - EXECUTION

3.01	Installation

A.	Protect all expansion joint component parts from damage during installation and placement of wall or ceiling materials and thereafter until completion of structure.

B.	Expansion joint systems shall be installed in strict accordance with the manufacturer's typical details and instructions along with the advice of their qualified representative.

3.02	Clean and Inspect

A.	Upon completing installation the contractor shall clean all exposed metal surfaces with a suitable cleaner that will not harm or attack the finish.  Contact manufacturer should questions arise regarding suitability of any cleaner type prior to its use.